## Slide 1: Real Solutions Product Introduction
Cartridge Safety Relief Valve - CSRV

## Slide 2: CSRV Overview
CSRV is an evolution of the SRV series of safety relief valves
Cartridge based design
Drop in replacement for SRV
Available in various configurations

## Slide 3: Features and benefits
Save money – the cartridge based design results in easier valve replacement
  The housing stays installed while the cartridges are swapped out
  No need to re-pipe

## Slide 4: Features and benefits
Stay safe – stay protected even during maintenance operations
  The dual CSRV + maifold combination allows the system to remain protected while the cartridges are swapped out

## Slide 5: Features and benefits
Save time – the CSRV will save you time
  No need to re-pipe during maintenance
  No need to re-pipe during an upgrade
  Cartridge replacement takes less than 5 minutes
  During the next maintenance interval upgrade to the CSRV and decrease your costs

## Slide 6: Safety Relief Basics
Used to prevent overpressure situations
Safely vent or re-direct refrigerant in the case of a overpressure situation
The mechanical equivalent of a fuse
Rated based on capacity (flow) and connection size
Available for liquids or vapors (CSRV is vapor only)

## Slide 7: Safety Relief Basics
Precision machined moving parts
Stainless Steel cartridge
Will not cold weld or corrode
Designed to open at a specific pressure

## Slide 8: CSRV Selection
Valve | Inlet | Outlet | Pressure Setting | SCFM (air)
CSR1 | ½” | ¾” | 150-400 | 130-290
CSR2 | ½” | 1” |  | 246-622
CSRH1 | ½” | ¾” |  | 463-1173
CSRH2 | ½” | 1” |  | 
CSRH3 | ¾” | 1” |  | 

## Slide 9: Selection Criteria
Safety relief valve should be set below design working pressure of the vessel
Safety relief valve should be set at least 25% higher than the normal operating pressure of the system
Pressure limiting devices should be set at less than 90% of the safety relief setting
Follow all local rules and regulations!

## Slide 10: Capacities
Per ANSI/ASHRAE 15 the discharge capacity is determined by:
C = F * D * L
  C = capacity in lbs/min
  F = 0.5 for NH3
  D = Outer diameter of vessel
  L = Length of vessel

## Slide 11: Typical Installation

## Slide 12: Cartridge Replacement
45-50 ft-lbs

## Slide 13: Summary
The CSRV is a proven extension of the SR series
The cartridge based design allows for easier maintenance
The CSRV will save you time
The CSRV will save you money
The CSRV will keep you safe

## Slide 14: Questions?