## Slide 1: HBLT-wire
Product Introduction

## Slide 2
The first ”real” Plug and Play sensor for the industrial refrigeration industry
Plug and play solution.
No dead zone – no calibration – no adjustment to standpipe
4-20 mA linear output or 4-20 mA P-regulation of valve
Alarm output - PNP-NO/NC.
An installation height of only 6” is required.

## Slide 3
Our goal is to innovate and to push the boundaries of the industry - and now you can reap those rewards!
One sensor works for NH3 or HFC refrigerants. The same sensor can be used in industrial or marine applications.
NH3
HFC

## Slide 4
Better, smaller, and more cost-efficient – this is the future of the refrigeration industry!
You can get it:
Cut and configured - free of charge
The ”IKEA” solution – cut it yourself

## Slide 5
Plug and play. No requirement for recalibration. No requirement for dead zone optimization.
Measures NH3 & HFC refrigerants: R22, R134A, R404A, R410A, R507, R717 & R718).
For marine installations: Can be used for marine applications, since measurement is not affected by contact with the metal surface of the overflow pipe.
Cut and configure: Flexible sensor wire, which is adjustable to a length of 300 to 4000 mm
Configuration by Windows App: Simple PC configuration for the specified length and refrigerant.
Product features:
Minimum installation height: Requires only 155 mm installation height.

## Slide 6
Smart split design - makes it easy to install and service. Fault detection on the electronics and/or replacement of the electronics can be carried out without releasing pressure on the system.
No dead zone: Dead zone limited to 0 mm.
Alarm: Alarm output can be set in a range from 10% to 100%.
Thread size: Available in ¾” NPT and ¾” BSPP.
Product features:
P-regulation: The possibility for direct regulation of modulating valves, pilot valves, or step motor valves.

## Slide 7
Measuring points:
20 mA / 100%
4 mA / 0%
Alarm point
Tank linear measurement – 4mA/0% … 20mA/100%
Programmable alarm point: 10-100 %

## Slide 8
Measuring points:
20 mA / 100%
4 mA / 0%
P-regulation in Alfa Laval plate heat exchanger
Programmable:
Set-point: 0-90 %
Alarm point: 10-100 %

## Slide 9
Electrical connections:
Pin 1 / 2: Power supply – 24 V AC/DC
Pin 4: (AO) – 4…20 mA linear or P-regulation of valve
Pin 3: (DO) – PNP – NO/NC
Pin 5: Not used (communication)
Delivered with 5 m cable with M12 plug on one end – flying leads on the other end.

## Slide 10
Cut & configure:
Tools required:
Adjustable wrench
2.5 mm hex key
Wire cutter
Tape measure

## Slide 11
Cut & Configure:
Tools required:
HBLC Tool (from website)
HBxC-USB (prog. Cable)
1) Sensor refrigerant should be input here
2) Sensor length should be input here
3) Enter the standpipe diameter here
4) Save by clicking “Set configuration”

## Slide 12
Installation in a standpipe:
Items / measures | DN40 (Ø48,3x2,6)
Tee (2) | DIN 2615-1
Bending 90°(3) | DIN 2615-1/Type 3
Welding connection (4) | Ø48,3x30 mm
Refrigerant | R718, R717, R507, R410, R134, R22
Max pressure | 53 bar
Pipe standard | DIN 10220
Pipe length (1) | L+114
Centerline | L
Welding connection - A | Ø48,3
Welding connection - B | Ø38,3
Installation guidelines:
Shut-off-valve recommended
Isolation of pipe recommended

## Slide 13
 | RTK | E+H | Hansen | Danfoss | HB Products [Wire sensor]
Refrigerant | R717, R22, R134A | R717, R22, R404A, R410A, R134A | R717, R22, R134A | R717, R22, R404A, R410A, R134A (R744*) | R717, R22, R404A, R410A, R134, R744, R507
Analogue output (AO) | 4-20 mA | 4-20 mA | 4-20 mA | 4-20 mA | 4-20 mA
Digital output (DO) (Alarm output) | No | NO | No | No | PNP, NO/NC (programmable)
P-regulation of valve | No | No | No | No | Yes, programmable by PC
Configuration/Calibration | Trimmer | Yes by HMI, HART or PC | Trimmer | Yes by HMI | Yes by PC
Bus communication | CAN-open (optional) | No | No | No | No
Display standard | No – but LED | No | No | No | No – but LED (LCD coming in 2014)
Display option | No | Yes | Yes | Yes | No
Measuring range | 150…4000 mm | 150…3000 mm | 510…4270 mm | 800…5000 mm | 300…4000 mm
Available length (L) | Can be ordered in any size 150…4000 mm | Can be ordered in any size 150…3000 mm | 510, 760, 1015, 1525, 2030, 2540, 3050, 3660, 4270 & custome lengths | Can be cut in any size 800…5000 mm | Can be cut in any size 300…4000 mm
Protection degree | IP65 | IP65 | IP65 | IP67 | IP65
Connection thread type | 1” RG | ¾”NPT, ¾”BSPP, 1”NPT, 1”BSPP | ¾” NPT | ¾”NPT & 1” BSPP | ¾”NPT, 3/4BSPP
Dead zone (bottom) | 0 mm | 0 mm | 16 mm | 115-240 (90) mm | 0 mm
Split design | No | Yes | No | Yes | Yes
Shipping size – l:1000 mm | 160x10x10cm-w: 10 kg | 130x15x15cm – W: 6 kg | 150x10x10 cm – w: 6 kg | 19x24x33 cm – w: 2,2 kg | 9,5x9,5x32 cm – w: 1,1 kg
Shipping cost – Denmark/Spain – l:1000 mm | 60 Euro | 47 Euro | 47 Euro | 36 Euro | 22 Euro
Installation height required | 420 + L | L+150…1000+230 mm | 337 + L | 220 mm | 155 mm
Standpipe size | Ø114 mm | ? | 3” (Ø76,2 mm) | 2-4” (Ø50,8-101,6 mm) | 1 ½” (Ø48,3 mm)
Require preparation before installation | No | Yes | No | Yes – approx 30 min | No – can be ordered in fix length at no extra cost
Required accessories for set-up and price | No | No | No | HMI Display | Only for special situations - Free software tool + programming cable (50 Euro)
Require 0% calibration | No | Yes | Yes – if not 3” standpipe and R717 | Yes – for dead zone 90 mm | No – Plug and play
Require 100 % calibration | No | Yes | Yes - if not 3” standpipe and R717 | No | No
Usable in marine installation | Yes | Yes | Yes | No (only with reference pipe) | Yes
Cable included | No | No | No | No | Yes – 5 m
Require special skills | No | Yes to some extend | No | Yes to some extend | No
Benchmark – Level sensors for industrial refrigeration